# DOMESTIC HOT WATER STORAGE TANK

### Domestic Hot Water Storage Tank

There shall be provided and installed Buderus indirect domestic water storage tanks, Model ____________, _____ gallon capacity each, and a continuous performance rating of _____ gpm based on a 130 °F temperature rise of domestic hot water.  The hot water tank shall be of welded high-grade rolled steel plate construction. The tank shall be fabricated with a flanged hand access cover, secured with eight bolts and a reusable gasket, for access to the interior of the tank for inspection and cleaning purposes. The tank shall be approved and listed domestic water storage tank.  The finished coating shall be unaffected by the chlorine content of the water, and be bacteriologically and hygienically harmless. Th tank shall have provision for insertion and attaching of either an electrically charged anode equipped with a self diagnostic monitoring system or a magnesium anode to protect the tank against corrosion.  The entire tank shall be insulated with 2" of high density non-CFC foam insulation, and wrapped with a sheet metal jacket. The metal jacket components shall be painted with a rust-resistant paint. The tank shall be furnished with screw-in feet to level the tank.  All interior surfaces shall be thermally shock resistant between -22 °F and 430 °F, without crack formation or chipping of the glass enamel protective barrier material.

#### Circulating Pumps

Circulating pumps for the Boiler, heating pumps and domestic hot water production shall be selected and supplied as specified.

#### Accessories

Contractor shall supply and install all necessary accessories for a complete and functional system as per the drawings and local code requirements. These accessories shall include, but are not limited to the boiler feed-water valve, backflow preventor, expansion tanks, air scoop, air vents, temperature and pressure gauges, valves, fittings power and control wiring.

Please consult Klimatrol Environmental Systems 905-454-1742.